# Repository Information
1. Name
  1. modular_device_base_3x2
2. Version
  1. 1.2
3. Author
  1. Peter Polidoro
4. Email
  1. peterpolidoro@gmail.com
5. License
  1. Open-Source Hardware
This board is the base of 3x2 format modular devices. It is a breakout board for the microprocessor, with connections for power, communication, and top boards.
# Images

# Schematic
./schematic/modular_device_base_3x2.pdf

# Gerbers
Save gerbers zip file and send to your favorite PCB manufacturer for fabrication.
./gerbers/modular_device_base_3x2_v1.2.zip

# Bill of Materials
## PCB Parts
./bom/bom_pcb.csv
Item	Reference(s)	Value	Quantity	Description	PartNumber	Vendor
1	C1 C2 C3 C4 C5	10uF	5	CAP CER 10UF 50V 10% X7S 1210	445-4536-1-ND	digikey
2	C6	0.1uF	1	CAP CER 0.1UF 100V X7R 1210	399-13229-1-ND	digikey
3	D1 D2	diode_schottky_15V_1A	2	DIODE SCHOTTKY 15V 1A DO214BA	LSM115JE3/TR13CT-ND	digikey
4	D3 D4 D5 D6 D7 D8 D9	diode_schottky_45V_10A	7	DIODE SCHOTTKY 45V 10A CFP15	568-11697-1-ND	digikey
5	L1	LED_5V_RED_RA	1	LED 2MM 5V RT ANGLE RED PCMNT	350-1712-ND	digikey
6	L2	LED_5V_GRN_RA	1	LED 2MM 5V RT ANGLE GREEN PCMNT	350-1717-ND	digikey
7	L3	LED_5V_YEL_RA	1	LED 2MM 5V RT ANGLE YELLOW PCMNT	350-1719-ND	digikey
8	MDB1	MODULAR_DEVICE_BASE_3x2_FEMALE	2	16 Position Header Through Hole Female Socket	S7049-ND	digikey
9	MH1 MH2 MH3 MH4	MNT_HOLE	4	Round Standoff Threaded 4-40 Aluminum 0.500in 0.187in	36-2027-ND	digikey
10	P1	PWR_JACK_2.5x5.5	1	CONN PWR JACK DC 2.5X5.5 8A T/H	CP-063BH-ND	digikey
11	P2	BNC_DOUBLE_RA	1	CONN BNC JACK R/A 75 OHM PCB	ACX1655-ND	digikey
12	P3 P5	HEADER_01X03_SMD_RA	2	CONN HEADER 3POS R/A SMD GOLD	A100890CT-ND	digikey
13	P4 P6	HEADER_01X02_SMD_RA	2	CONN HEADER 2POS R/A SMD GOLD	A100903CT-ND	digikey
14	P7	HEADER_01X03_RA	1	CONN HEADER 3 POS RA 2.54	732-5336-ND	digikey
15	P8	HEADER_01X02_SMD_RA_UNSHR	1	CONN HEADER 2POS .100in SNGL SMD	SAM10781-ND	digikey
16	R1	6.19k	1	RES SMD 6.19K OHM 1% 1/2W 1210	P6.19KAACT-ND	digikey
17	REG1	CONV_DC_DC_5V_1A	1	CONV DC/DC 1A 5V OUT SIP VERT	945-1395-5-ND	digikey
18	SW1	KT_SWITCH	1	SWITCH TACTILE SPST-NO 1VA 32V	CKN1860CT-ND	digikey
19	TEENSY1	TEENSY_3.2	1	DEV TEENSY 3.2 13736	1568-1231-ND	digikey
20	U1	MAX6817	1	IC DEBOUNCER SWITCH DUAL SOT23-6	MAX6817EUT+TCT-ND	digikey

## Additional Parts
./bom/bom_pcb_add.csv
Item	Function	Quantity	Description	PartNumber	Vendor
1	MODULAR_DEVICE_BASE	1	USB 2.0 Cable A Male to Micro B Male 2.00m Shielded	AE10342-ND	digikey
2	POWER	1	AC/DC DESKTOP ADAPTER 24V 90W	62-1187-ND	digikey
3	POWER	1	30 WATT DESKTOP POWER SUPPLY 24V	EPS594-ND	digikey
4	POWER	1	CORD 3COND NEMA PLUG 320-C5	993-1037-ND	digikey
5	CONNECTORS	1	14 Positions Header Unshrouded Breakaway Connector 0.100in 2 row SMD	A106625CT-ND	digikey
6	CONNECTORS	2	24 Positions Header Unshrouded Breakaway Connector 0.100in 1 row Through	S1011EC-24-ND	digikey
7	CONNECTORS	1	CONN JUMPER SHORTING GOLD FLASH	S9001-ND	digikey
8	CABLE	1	CABLE USB-A TO MICRO USB-B 2M	AE10342-ND	digikey

## Vendor Parts Lists
./bom/digikey_order.csv
./bom/digikey_order_pcb.csv
./bom/digikey_order_pcb_add.csv